What is 3D printing?
3D printer technology has been evolving since the process was first patented in the 1980’s. Since then, many different iterations have been created that rely on vastly different processes. However, the base principle remains the same. The output is a 3D model commonly, but not excluded to a plastic material, that is conceived through the formation of successive layers. Alternatively it is known as additive manufacturing, opposed to CNC milling, which forms objects by cutting away raw material.

If we take a step back and look at 3D printing as a whole, we can notice it is composed of several key parts. The first is the printing surface. Whether it be a heated aluminum sheet or a glass pane covered in tape, the plastic needs a surface to begin printing on. This surface is commonly referred to as the printing bed. The next component is the raw material. Plastic is a very common material for printing and we usually encounter it in two raw forms, either as a liquid or as rolled wire known as filament. The next component is a device that takes the plastic in its raw form and transforms it into its final form and the last component is a mechanism that places the plastic on the printing bed. If we put all these pieces together, we get a machine that produces an object in three dimensional space.

There still lies a software aspect to 3D printing. Typically, the process of designing and printing a model begins with a computer aided design program (CAD). These programs are very user friendly and allow you to see how the model will look before being printed.

Afterwards, the model is typically exported as an STL file before being converted into G-code, which is fed directly to the printer. Before the printing can begin, there are many decisions that need to be made, such as what material will be used, the resolution of the print, fill density, whether to use a heat bed, what temperature to use in order to avoid print deformations, etc. The printer also needs to be properly prepared and calibrated to achieve a successful print.

A print can last anywhere from a few minutes to a few days depending on the size, complexity and resolution of the print. The final step after the printer is finished is to finalize the part. Since the printer layers materials on top of each other, the print won’t be as smooth as a molded part. Many like to sand, paint or dip the printed models in various chemicals to achieve various effects.

In all, the process is long and differs between different printers. Many things can be automated, calibration for instance, however this raises the price of these machines and make them more inaccessible to the public.

The reason printers have become so popular and accessible is because of how many of them are open-sourced. The aim of many of these projects is to create a reliable and friendly printer that can be used as a learning tool.

Types of 3D Printers
Stereolithography (SLA)
This method of printing is one of the oldest and simplest to implement. The basic premise is to have a UV laser cause a chemical reaction in a vat of photopolymer resin to form polymers. The laser draws a 2 dimensional shape and builds layers to form the complete object. This technology is rarely used to produce final products, but rather to rapidly prototype and visualise designs.

Digital Light Processing (DLP)
This process is very similar to SLA printing. DLP printers dispose of the laser and use more conventional sources of light, most commonly projectors. This light shines on a vat of liquid plastic resin which hardens quickly when in contact with large amounts of light. The object is created layer by layer exactly like the SLA method. The advantage it has over SLA printing is that it is much faster. Unlike the SLA printer where the laser slowly creates a layer of plastic, the DLP printer creates an entire layer at once.

Pros:	Very high quality prints
Capable of making small parts

Cons:	The resin is expensive
The finished product maybe brittle and breaksdown under UV light
Takes a long time to print

Fused Deposition Modeling (FDM)
This process takes advantage of thermoplastics. Objects are built from the bottom up by heating a thermoplastic filament to its melting point and extruding it layer by layer. This has many advantages over its counterparts, it allows for printing of more materials in one build, the plastics have better chemical and physical properties and the filament is much cheaper than vats of resin.

Pros:	Can make low resolution parts faster and stronger
Low cost plastic filament
Higher quality plastics
Capable of printing many materials at once

Cons:	Lower quality prints

There are many more methods and processes, each more advanced than the last. However, the two leading technologies are DLP and FDM printing.

A general comparison between the two leading technologies would show that DLP printing can make prints of incredible detail at a cost of physical robustness, while FDM prints are much stronger but loose on quality of print. A common conclusion is that both are useful in an engineers workshop, they both have their use cases depending on the task on hand.

Variations of FDM Printers
With FDM printing, a plastic is heated to its melting point and extruded in a specific pattern. In order to achieve a pattern, a mechanical machine is required to draw it with the plastic. This mechanism has to be able to move in 3 dimensional space to produce the 3D structure. There are many schools of thought to achieve this. The two leading ones are Delta and Cartesian printers.

Delta Printer
These printers typically have three vertical axises, each axis allows the up and down movement of a rod. All three rods connect in the center where the extruder is located. To calculate the position of the printer head, the use of trigonometric functions are necessary.

Pros:	Very fast movements
Large printing volume
Small footprint

Cons:	Complex to build, maintain and calibrate
Experience extruder problems as the motor is separated from the printer nozzle

Cartesian Printer
The reason these are so popular is because they are simple. They have three axises, each moves in either the x, y or z direction. Therefore the position of the extruder is already directly accessible, as apposed to the delta printer where extra calculations are necessary. To further categorize the Cartesian printer, we can divide them into printers where the bed does the x motion and the extruder does the y and z motions or the bed does the z motion and the extruder moves in the x and y directions. These types of mechanisms are also commonly seen in CNC mills and even 2D printers except of course without the z axis.

Pros:	Low cost
Simple to build, maintain and calibrate
Can print with great accuracy

Cons:	Larger than delta printers
Slower than delta printers

There are many other methods of printing; Six-Axis printers, SCARA printers and Polar printers. However, as the complexity increases, so does the likelihood of a failed print or unforeseen problems.

Modeling Software
The process that begins from the conception of an idea to the finalized product requires many tools and softwares. Usually the first software that needs to be chosen is the 3D modeling software.

The decision as to which software will be the best needs to be based on your hardware, precision, experience and budget. Since 3D printing has been popularized, many user friendly modeling softwares have been released such as Cura, Craftware, 123D Catch and TinkerCAD from Autodesk and 3D Slash to name a few. These allow beginners to easily access the market and try their hand at designing. However they often lack functionality or precision.

More advanced modeling software includes Sketchup and the program that we will be using, FreeCAD. The last group of modeling softwares include professional suites, which require capable hardware and come at a larger price.

FreeCAD is a free open-source parametric 3D modeling application that runs on most operating systems. The largest advantage is that it is parametric based, meaning all objects are controlled by parameters allowing for very precise builds. The downside is that there is a learning curve to overcome and might be difficult to produce error free builds without prior experience with CAD software.

After your model is complete, it will need to be exported as an STL(STereoLithography) file. This format is an agreed upon norm, the model is described by its triangulated surface geometry. It is convenient to first convert the solid model into a mesh before exporting as an STL, however it is not always necessary.

A very useful software is Slic3r. Slic3r, as the name suggests, slices the object into layers and decides the best way for the printer to maneuver the print. This software is printer specific, you need to provide all information about your printer including nozzle thickness, print quality, temperatures etc. Then based on the information provided, the Slic3r converts a STL object into G-code, which are step by step instructions for the 3D printer.

The G-code can be loaded into the printer interface. The printer interface shows you information such as sensor readings, number of layers printed, estimated time left and allows manual control over the printer through G-code in the terminal or through a more friendlier user interface.

This covers the software portion of 3D printing. Due to the nature of 3D printing being open-source, so are most of the softwares. That is why many come at no price at all and are multi-platform. Many times it is useful to have several programs installed depending on the task at hand. For instance TinkerCAD allows for very quick modeling and having a print ready in minutes, whereas FreeCAD requires more attention to detail and the process of designing is much more time consuming, but allows for precise models.

Calibration and Maintenance
Calibration is a very important to have well printed parts. There are several calibration procedures that need to be done only once, and others that are more routine. For instance, when a printer is first turned on, the amount of current going into the motors needs to be tweaked, the thermistors need to be checked if they are showing accurate temperatures and the endstops need to be correctly positioned. Other routine procedures comprise of belt tensioning, bed leveling, extruder maintenance, motor scaling (making sure that 1mm is 1mm) and checking that all the cables are correctly connected and not damaged. These steps are important to not only ensure the print will go smoothly, but also as a safety precaution.

This process can be enduring, however there are many ways to automate these processes. Self-calibration can allow for more consistent prints by avoiding human errors and can greatly speed up the preparation time of the printer.

Endstop Scaling Calibration

Bed Leveling

Belt Tensioner

Modularity
Sooner or later the parts will need to be replaced or upgraded. Having a printer that can easily disassemble without unscrewing twenty bolts will prove to be more comfortable to work with. However, sturdiness of the printer is obviously a priority. The goal is to have a printer that is easy to disassemble, yet doesn’t sacrifice on quality of print.

Applications of 3D Printing
In its early days, 3D printing was seen as the successor to the production line. However, because of its high production costs, it has found other more practical uses. The traditional method of mass producing plastic parts includes creating molds and injecting them with plastic. This is a quick and reliable method and remains to be one of the most efficient mass production processes. However with each new part, a new mold has to be created. This is the advantage of 3D printers, they allow each print to be easily customized without long prep work. The process of mass production of customizable elements to create differentiating products is called mass customization and is almost exclusively possible because of 3D printing technology. An example would be the production of custom fit prosthetics or smart phone companies providing personal designed phone cases.

3D printers are perfect for rapid prototyping as they can print multiple pieces at once and don’t require lengthy special prep work. Prototyping can be rather tedious with other methods such as with molding, where for every iteration of the product a new mold has to be created. Printing makes the development of new products and research much easier and more accessible as specialized tools are not needed.

The effects of 3D printing are quickly spreading to medical applications as well. Today we can order custom fit 3D printed prosthetics, but in a matter of years bio-printed organs will become accessible. 3D printers have also shown up in the apparel and jewelry business as artists have new ways of expressing their ideas. The Zero-G printer can print in zero gravity, this makes it possible to simply send a 3D printer into space and create tools only when they are needed, saving on fuel and costs. The 3D printer has become widespread and are a crucial part in many processes.

Stepper Motors
X/Y-axis
The X and Y axes are driven by a belt, which allows for quick changes of direction.

Z-axis motors
The main purpose of these motors is to drive the Z-axis. The motors will drive lead screws, which in turn raise or lower collars attached to the X-axis. The movements are small and incremental, meaning it will not be rapidly changing directions like the other axes, this is why using a lead screw is more practical than another belt drive.

Let us assume we will be using a 4 lead M8 lead screw with a thread density of 52 threads per 10cm. Meaning to raise an object 1 cm, we need to rotate the screw 1.3 times.

We will be using the work energy theorem to calculate the torque needed to lift the X-axis.

Work needed to be done to lift the X-axis:	mgh_1 % + % W_h % + % W_other% = % mgh_2 %

,where	F_x % = % mg is the force of the X-axis due to gravitational acceleration
W_h is the energy needed to change the X-axis height
W_other % = % - %mu F_n %DELTA h is the energy lost due to friction

After reconfiguring our equation, we get the following:	W_h % = % F_x %DELTA h % + % %mu F_n %DELTA h

Work needed to be done to rotate the lead screw an angle of %theta :	W_%theta % = % %tau %DELTA %theta
,where	W_%theta is the energy needed to rotate the lead screw
%DELTA %theta is the angle of rotation
%tau is the torque of the motor

Relationship between %DELTA h and %DELTA %theta :	%DELTA h (1.3) % = % %DELTA %theta

With the above relationship, we now know how the raise height of the X-axis is dependent on the angle of rotation of the lead screw. Therefore we can compare the energy needed to rotate the shaft to the energy needed to lift the shaft.
If we combine the three above equations, we get the following:	%tau % = % 1 over { 1.3 } left ( F_x % + % %mu F_n right )

Since we want to know the maximum torque we need supplied by our motor, we need to find when the potential energy is increasing. Therefore the maximum torque required by our motor will be encountered when the X-axis is being raised. We will now only examine this one scenario.

Since the motion is strictly vertical, we know that the normal force of friction is parallel to the lead screw, more specifically we know that it is equal to F_x . This gives us the new equation:

%tau % = % {F_x ( 1 % + % %mu)} over { 1.3 }	in [ Ncm ]

As we can see, the torque needed to drive the Z-axis is rather small. Even with a large weight of the X-axis and a large friction coefficient of 15[N] and 0.3 respectively, we need a torque of only 15[Ncm]. If we have two motors driving the Z-axis, the torque on an individual motor will be halved, further reducing the maximum torque.

Based on the above calculations, we may conclude that two small stepper motors of a torque of at least 10[Ncm] will suffice at driving our system. However, since one small mistake can ruin an entire print, larger motors are preferred. A larger motor can potentially avoid overheating as it may be active for many hours and more torque guarantees the motor does not skip. Also since the motor is attached to the frame in a stationary position, the additional weight added to the build by the motors does not affect its performance.